## Slide 1
The H2RG infrared detector: introduction and results of data processing on different platforms
Andreas Jung (ESA), Pierre-Elie CROUZET (ESA)

## Slide 2: Outline
The H2RG infrared detector
  Readout chain
  Specifications
  Way of sampling
  Data processing requirement
Data processing
  Data processing pipeline steps
  Profiling results
Conclusion

## Slide 3: Infrared detectors: H2RG
State of the art detector already used for
  Hubble Space Telescope, Wild Field Camera 3
  NIFS Gemini north (Mauna Kea, Hawaii)
  JWST Near Infrared Spectrograph
  ESO, X-shooter (spectrograph), Paranal

## Slide 4: Readout chain
JADE: JWST ASIC Drive Electronics
H2RG detector
SIDECAR ASIC
Clock generation
Bias generation
Digital interface to instrument electronics
Low power operation
  Less than 150 mW at 100 kHz, 32 channel, 16 bit ADC
JADE2 card

## Slide 5: Specifications
Company | Teledyne
Detector name | HAWAII-2RG
Pixel size | 18 µm
Number of pixels | 2048 x 2048
Readout frequency | 100kHz or 5Mhz
Number of outputs | 1,4 or 32
Frame size | Full frame, window mode
Reference | Pixels or one channel
Reset scheme | By pixel, by line or globally
42s at 100kHz
1.36s at 100kHz
1 output
output 1
output 32
32 blocs of 64*2048 pixels
1 bloc of 2048*2048 pixels
2048 pixels
2048 pixels
4 rows and 4 column of reference pixels

## Slide 6: Way of sampling
goal: remove common noise
Readout : C.D.S
(Correlated Double Sampling)
reset
Total integration time
integration time
goal : decrease readout noise
Readout : Fowler(N)
Total integration time
integration time
Multi-accumulation
Total integration time
integration time
No. of burst
goal: check linearity (cosmic ray)
Readout : up the ramp
Total integration time
integration time
frames

## Slide 7: Way of sampling
Example of one acquisition:
  Non destructive readout (not like a CCD)
  Evolution of the signal for one pixel
Data processing is needed to compute final signal and its uncertainty

## Slide 8: Objective
The objective of the investigations performed at ESTEC were:
Estimate the CPU processing needs for the pre-processing
Evaluate the impact of the pre-processing steps on the performance
…to be able to make a trade-off for the selection of the needed pre-processing steps on-board to reach the performance (signal to noise ratio) requirements.
To be done

## Slide 9: on-board pre-Processing pipeline

## Slide 10: Saturation detection, Co-adding, (Super-)Bias subtraction
Saturation detection
Objective: Detect if a pixel has gone into saturation to stop with the estimation of the flux in the later steps. Input: One value for each channel.
Co-adding
Objective: reduce read-out noise Sum the frames of each group (typically 1-8 frames).
(Super-)Bias subtraction
Objective: Remove pixel-to-pixel variation in offset
Subtract a bias frame (2048x2048) from the frame obtained from the detector.

## Slide 11: Non-linearity correction
Non-linearity correction
Objective: correct for non-linearity of the detector
A 4th order polynomial is used for the correction with a single set of coefficients for each channel.
Results obtained thanks to Andreas Jung (TEC-SWE)

## Slide 12: Reference pixel subtraction
Objective: remove common noise
For each of the 32 channels: calculate the mean (sigma clipped) of the odd and even pixel of the first 4 and last 4 rows and subtract it from the odd and even pixel of the frame.
Running average (+-2 rows) of the lateral pixel
Results obtained thanks to Andreas Jung (TEC-SWE)
i.
ii.
1/f correction using FFT is possible too, no major difference in CPU speed.

## Slide 13: Cosmic ray detection and Linear least square fit (progressive)
Cosmic ray detection
Objective: Estimate flux and detected disturbances by comic ray
For each pixel:
  Estimation slope and intercept (linear least square method)
  Extrapolation next point
  Add noise to interpolated point
  Flag if next point is above threshold
  Subtracting running mean of all the following differences found (∆)
  Continue estimate slope and intercept
∆

## Slide 14: on-board pre-Processing pipeline: Main loop
First results of Profiling focuses on main loop.
Note: Same code used for profiling as well as for performance evaluation with simulator data.

## Slide 15: Profiling results of on-board pre-Processing pipeline (1/2)
Implemen-tation in… | Leon AT697E @ 80 MHz | Maxwell SCS750 @ 400MHz | @ 800MHz | Memory usage
Floating point | 28.2s | 5.9s | 4.5s | 68.6 MB 84.6 MB (with bias)
Fixed point | 21.5s | 4.6s * 4.7 (wrt Leon) | 3.4s * 6.3 (wrt Leon) | 52.6 MB 60.6 MB (with bias)
“only” -24% in CPU time
however higher electrical power consumption!
Results for main loop for one (co-added) frame of 2048x2048

## Slide 16: Profiling results of on-board pre-Processing pipeline (2/2)
Processing step | Leon @ 80 MHz | SCS750 @ 800 MHz | Integer Ops | Float Ops
 | 0.7 | 0.14 | 7 | 0
 | 0.9 | 0.33 | 7 | 0
 | 3.6 | 0.29 | 26 | 0
 | 0.7 0.9 | 0.26 0.22 | 5 7 | 0 0
 | 13.3 | 1.58 | 57 | 4
 | 3.0 | 1.07 | 22 | 0
 | 1.7 | 0.63 | 12 | 0
Per Pixel
Total time [s]
Square root calculation!
FPGA vs. DPU: in addition 5-10% extra CPU time if performed on DPU

## Slide 17: Summary
Everything set up to do now the performance tests.
Same code for profiling and performance tests (and for floating point and fixed point)
CPU needs for each pre-processing step and overall need for main loop known on different target platforms: Leon AT697E 21.5s Maxwell SCS750 3.4s – 4.6s Memory usage 53MB or 61MB (with bias) BUT: Additional CPU time needed for Compression and IOs (from FPGA to DPU and DPU to Mass memory)